South Dakota School of Mines and Technology

Department of Materials and Metallurgical Engineering

MET 320	HQ 1	MI 220

9:00 AM 		Oct 5, 2006

ASK NO QUESTIONS

- If there seems to be a problem, note the trouble, make a reasonable assumption and work the problem under your assumed correction.

- There has been no attempt to write problems with errors.

CLOSED BOOK and NOTES and NO CALCULATORS

- Algebraic Answers Preferred

- Leave R in the equation but write out its value to achieve proper units.

UNITS (Algebraic answers should be left in a form to obtain these units

- q, w, U, and H [=]  Joules

- S [=] J/K

- V[=]Liters

- T  [=] K

- P [=]  atm

SHOW ALL WORK ON THIS SHEET.

- Turn in only the problem sheets with the problems on them.

- Keep or discard all other paper

5 PROBLEMS OF EQUAL VALUE

- Work the problems that seem the easiest for you first.

- Twenty moles of ideal monatomic gas at 1000 K having a volume of 100 liters perform 1000 J of work while isothermally and reversibly expanding.  Show how to compute the

  - Initial gas pressure, P1

  - Final gas volume, V2

  - U

  - H

  - S

- Ideal diatomic gas in a cylinder at 0.8 atm and 280 K is adiabatically compressed to 1/10th its original volume.

    - What are the final T, P

    - Find q, w, ∆U, and ∆H for the process?

    - What would be the major difference if the ideal gas were monatomic?

- A heat pump is operating between sinks at 300 K and 200 K on the surface of Mars in a manned spacecraft.  How much theoretical work energy is needed every second to provide 1000 J per second to the craft?

- One mole of ideal monatomic gas at 300 K and 1 atm receives 1000 J of heat while having 500 J of work performed on it.  What is the final temperature of the gas?

- One mole of ideal gas at 1000 K and 10 atm is expanded isothermally to 10 times its original volume while doing half the maximum possible work. The gas is always in thermal equilibrium with a heat sink also at 1000 K.  Find the S for the

    - Gas and

    - Sink

    - Gas and Sink (total)

Scratch paper – Detach this sheet and take with you – It will not be considered for grading.