South Dakota School of Mines and Technology

Department of Materials and Metallurgical Engineering

MET 320	HQ 2	Nov. 18, 2010

1.	Write the

a) 	Remaining three Fundamental Equations for a closed system:

dU = TdS – PdV

dH = U + PV =

dA = U – TS =

dG =

- So-called Other Thermodynamic Relations obtained from dU = TdS – PdV

- Maxwell Relation obtained from dU = TdS – PdV

- Definition of Chemical Potential,

2.	Show how to calculate the temperature when the pressure of water vapor above water is 10 atm. Water’s boils (1 atm) at 100 (C.

3.	Show how to determine the  for the following reaction at 1200 K from the data in the text appendices.  Show all values and equations needed.

1200 K	Cl2O3 (S)+ 2Al(L) = Al2O3 (S) + 2Cr(S)

298 K

4.	How many moles of CO2 would be required to pressurize a volume of 22.4 liters to 73 atm at 304 K?

Scratch Paper – detach and take with you.