Title:  Shaft Model variables

Subject:  Heat transfer coefficient “h”

From:  Lisa Schlink

The heat transfer coefficient was evaluated using the Ranz – Marshall Correlation.

Nu = hDi/k = 2+.6Re.5 * Pr.33

Therefore:

h = Nu(k/Di)

Where:

Di = particle diameter (m) = .02

k = thermal conductivity (Wm-1K-1) = (Cp+5R/4)/MWH2 = 4.016*103

Re = Reynolds number = Gg*R*Tg/P  = 117.186

Pr = Prandtl number = Cp/k = 1.515*10-3

 = Viscosity (Jm-3s) = .195

Using the equations above, a value of 5.547*105 was calculated for h.

The attached worksheet shows all variables, equations, and values for individual steps.

# Footnotes

The Making, Shaping, and Treating of Steel.  Editor Richard J. Fruehan.  11th Edition, AISE Steel Foundation. page 56, table 2.4.

The Making, Shaping, and Treating of Steel.  Editor Richard J. Fruehan.  11th Edition, AISE Steel Foundation. page 56, table 2.3.