To: Dr Howard

From: Anirudha Mahajan

Title: Shaft Model Information

Topic: Mass transfer Coefficients of H2 and H2O

Date : 03/27/02

General

R = 82.03 cm3.atm/mol/K

V = 117.97 cm/sec

Diameter of the particle, D = 1 cm

Pressure, P  = 1 atm

Tg = 1000 K

Density

Mwt H = 1 gm/mol

 H2 = 1.22 e-5 gm/mol

Mwt. H2O = 18 gm/mol

 H2O = 0.000195 gm/mol

 =  .0001 gm/cm.sec

Diffusivity H2, Diff H2 = 10.82 cm2/sec [1]

Diffusivity H2O, Diff H2O = 2.83 cm2/sec [1]

Reynolds #

Re H2 = 14.28

Re H2O = 228.49

Schmidt #

Sc H2 = 0.758

Sc H2O = 0.181

Mass transfer coefficients

k H2 =  44.012 cm/sec

k H2O =  20.185 cm/sec.

Suggested Values : Same as above.

References:

- E. T Turkdogan, “Fundamentals of Steel Making”, pp87